## Slide 1: SDR 3-Aug-2016
Part 1 – Overview
G0RVM

## Slide 2: What is SDR?
Software Defined Radio
A/D conversion of RF spectrum
One or more parts of RF spectrum simultaneously converted
Some analogue RF & IF stages still necessary / best done ‘traditionally’
‘Heavy-lifting’ done in fast FPGAs
Filters, modulation etc performed in software / programmable DSPs

## Slide 3: What is SDR?
ADC/DAC
DSP
Multi purpose computer
Analogue domain
Digital domain
Modern SDR places ADC/DAC as far to the left as possible
Avoids VFO, LO IF conversion, bandpass filters
Needs fast ADC/DAC
High data rates

## Slide 4: Why SDR?
With black box radio’s capacity for change is very limited
  buttons, knobs - fixed
  scope for filtering restricted – e.g. new multi-notch and noise reduction
  new modulation schemes not possible. E.g. Adding SSB to FM only radio
Software can easily be changed
  its flexible
  reduced obsolescence
  greater scope for experimentation
  convergence of analogue and digital domains
  greater sensitivity and selectivity

## Slide 5: Why SDR?
Interfacing simplicity:
  sound card interfaces – gone
  CAT cables – gone
  multiple ground-loops – gone
  different pin-outs, connectors and levels - gone
Virtual cabling rules! 
  interfaces can span geographies
Virtual receivers
  listen/watch multiple bands simultaneously

## Slide 6: Why SDR?
Filters:
  brick-walls
  wide, narrow
  user-definable
  multi-notch etc
  new software can improve filters, add new filters…
Potential to operate remotely
See signals not just hear them!
  monitor a band visually for activity
  panadapters, waterfalls, audio spectrum
  new displays added easily by developers

## Slide 7: Why SDR?

## Slide 8: Why SDR?

## Slide 9: Why SDR?
Simpler to use:
  TS-990 vs SDR comparison (next slide)
  why have all those buttons?
  just show the ones relevant for what you are doing!

## Slide 10: Why SDR?

## Slide 11: Why SDR?
Small and light!

## Slide 12: Why SDR?
Several manufacturers
  ANAN – Productised TAPR boards – Hermes, Angelina…
  Flex Radio
  Airspy, RTL-SDR, Funcube etc (Receivers)
Kits readily available
  TAPR
  SDR-Kits
  etc, etc lots of them...
Can be cheap or expensive
  But always significantly cheaper than ‘traditional’ radios

## Slide 13: Why SDR?
But you:
  want knobs and not to use a computer
  well that’s ok too 

## Slide 14: IQ Signals
IQ tutorial (19 mins)
  https://www.youtube.com/watch?v=h_7d-m1ehoY

## Slide 15
The End
Thank you